## Slide 1: System of Networked Sensors for Detection and Characterization of Underground Activity Final Product Presentation
Team 1: Tyler McKean, Augustus Standeven, Vulindsky Fanfan, Yohannes Kidane
Technical Manager : Dr. Tomas Materdey
Customer Mentor: Cpt. William Shepherd
This Photo by Unknown author is licensed under CC BY.

## Slide 2: Team Members
Tyler McKean
Augustus Standeven
Vulindsky Fanfan
Senior EE student
Senior EE student
Senior EE student
Yohannes Kidane
Junior EE Student

## Slide 3: Problem Definition
Designing a system of networked sensors for detection and characterization of unauthorized underground activity.
Capstone Project Requirements:
  Provide security for government property
    Military bases at home/abroad
    Government facilities
    National Border Security
Portable, durable, and unobtrusive
Able to cover a 100-meter radius
Cheap, Inexpensive Components
Wireless Network of sensors
Self-contained power source
Able to process data and categorize types of signals
  i.e., determine the likelihood of whether a signal received was from a passing truck or from a tunnel being dug.
Able to send processed signal data to a smartphone/laptop for user to interpret data

## Slide 4: System Diagram
Geophone Sensors with DC Offset PCB
  Passive Vibration sensors will be offset by 1.65V to capture peaks and troughs of oscillations.
Arduino Due
  12-bit Resolution for A/D Conversion
  Sample Rate at 500Hz
  Serial communication via USB port to Raspberry Pi for data logging.
Raspberry Pi w/ LED screen
  Data logging of Serial data from Arduino.
  Python scripts that Preprocess logged data and Extracts Statistical and Analytical Features that are imported into a KNN Machine Learning Model.
  Displays predictions of Vibrations to GUI, which includes History tab for previously occurred events.
Power Brick Battery
  Provides 12V 6000mAh/5V USB DC voltage

## Slide 5: Design Improvements
First Prototype Design
Second Prototype Design

## Slide 6: Design Improvements
All Components tied together, hardware has changed
Replaced AD2 with Arduino for ADC of vibrations data
PCB connected to Geophones
2-meter length insulated wires for Geophones
Raspberry Pi gathers the vibration data and displays it to GUI
Introduced Power Brick battery to make system portable
Initial Prototype
Final System Design

## Slide 7: DC Offset PCB
Functionality:
  Reasoning:
    Provide DC Offset to Geophone vibrations
    Without DC Offset, Arduino would only capture the peaks and not the troughs of the oscillations
    Allow Arduino to capture full oscillation information
  Equal resistor values will lead to voltage divider of Vref/2
  Digital values range from 0-4095 and will be centered around (2^12)/2 => 4096/2 = 2048
Results:
  PCB measurements vs expected values have low tolerance
  Observed values from Arduino show 3 geophones (red, blue, green) centered just above 2040
  PCB functioning as intended
Digital Value
Time

## Slide 8: Collecting Samples
Performed Signal Capture to obtain 1215 samples across 5 different Vibration Classes
  243 samples/each
Recorded three 81 sec long observations
Preprocessed in MATLAB to sparse data into 27 - 3 sec observations
27 x 3 Geophones = 81 observations
3 runs x 81 = 243 samples
Time performing Test:
3 mins per run
15 runs total
~ 45 mins - 1hr total test length

## Slide 9: Design Validation Tests
Test #1: Machine Learning Model
Performed by: Tyler/Vulindsky/Augustus
  Extract 32 Features from large set of signals
    Mean, Max, RMS, etc...
  Use data to train ML model in MATLAB
  Validate same model/data in Python
  Compare results from MATLAB/Python
Problem Statement :
  Classify vibrations to 70-80% accuracy
  Build a Signal Library to classify

## Slide 10: Design Validation Tests
Test #2: Data Acquisition & Logging
Performed by Augustus/Tyler
  Interconnections between Arduino and Raspberry Pi subsystems
  Display vibration data to the LCD Display of Raspberry Pi
  Additionally, saving the data to a .csv file that will be accessed by Python

## Slide 11: Design Validation Tests
Test #3: Battery Life of Power Supply
Performed by Tyler/Yohannes
  Verify the Power Brick total battery life
  Power Ratings: 12V 6000mAh/5V USB
  Raspberry Pi: 5V/2.5A
  Arduino Due: 3.3V
  Power Daisy Chained from Battery-> Raspberry Pi -> Arduino Due
  Calculated length: 15 hours
TalentCell Rechargeable 12V 6000mAh/5V
12000mAh DC Output Lithium-Ion Battery Pack

## Slide 12: Validation Results
Test #1 Results
Performed by: Tyler/Vulindsky/Augustus
  Extract 32 Features from large set of signals
    Mean, Max, RMS, etc...
  Use data to train ML model in MATLAB
  Validate same model/data in Python
  Compare results from MATLAB/Python
Problem Statement :
  Classify vibrations to 70-80% accuracy
  Build a Signal Library to classify
Part of Machine Learning Toolbox
Uses Supervised Learning to train different models of data - provided known inputs with known classes
  UI allows us to train multiple models for reference to which model fits our expected vibration signals

## Slide 13: Validation Results
Video shows data values captured and converted Arduino and serially sent and saved by Raspberry Pi
Battery at Full Charge
  Data acquisition started at 6:15pm and saved to .csv file on Raspberry Pi
  Last recorded timestamp around 4:50am next morning
  About 10 hrs 35 mins of Battery life
Total test time ~ 11 hours
Test#2 & 3: Data Logging and Battery
Initial recording time: 6:15pm
Final recording time: 4:50am

## Slide 14: Real-Time Vibration Detection
Serial Import
Data Preprocessing
Feature Extraction
Machine Learning Algorithm
Display on GUI

## Slide 15: GUI
GUI made in Python
  Sensor tabs to display what each sensor predicts
  History tab to look through previously classified signals and what time they occurred

## Slide 16: Final Deliverables
9 Geophone Sensors
DC Offset PCB
Trained KNN Model that characterizes known vibrations to an 89% accuracy
Arduino Due & Raspberry Pi 3 B+
6000mAh Lithium-Ion Power Brick Battery
GUI that displays real-time data analysis to User via touch screen
OneDrive folder with all software so that next team could continue and impove project next year

## Slide 17: Final Budget & Components
Vibration Data Acquisition
  Geophones
  Arduino Due
  Raspberry Pi 3 B+ with LCD Display
Data Analysis
  Altium Designer
    PCB Design and Simulation
  LTSpice/PSPICE
    Filter/Amp Circuit Analysis
  Matlab Toolboxes
    Signal Processing Toolbox
    DSP Toolbox
    Machine Learning Toolbox
MATLAB
  Classification Learner for ML model validation
  Preprocessing/Feature Extraction
Python
  GUI Development / Data Logging
Arduino IDE
  ADC of Arduino Due
SM-24 Geophone
Raspberry Pi 3 B+ w/ LCD
DC Offset PCB
Arduino Due
Power Brick Battery

## Slide 18: Project Management

## Slide 19: Team Roles & Communication
Team Members
Cpt. William Shepherd (Stevens Institute of Technology
    Customer Mentor
Dr. Tomas Materdey (UMass Boston)
    Technical Manager
Tyler McKean (Senior EE Student)
    Time Management, MATLAB/Python Feature Extraction, Classification Learner, Arduino Due, PCB
Augustus Standeven (Senior EE Student)
    Communications, MATLAB/Python Scripting, Signal Library, Raspberry Pi, Data Logging
Vulindsky R. Fanfan (Senior EE Student)
    Machine Learning, Python Implementation, GUI development and integration, Real time functionality of the system, Data Capture
Yohannes Kidane (Junior EE Student)
    Filter/Amp Design, Power Supply Management
Methods of Communication
Weekly Meetings
Team Meetings : Mon/Wed/Fri 10:00-4:00 PM
CM/TM Meetings: Mon/Fri 3:00-4:00 PM

## Slide 20: Ethical Considerations
Engineering Design Ethics
Safety
IEC 60478 - Stabilized Power Supplies, DC Output
    Right supply voltage to each component,
    Reassuring electrical safety as to not injure user or damage hardware.
    Use insulated wires
    Assure safe connections to onboard pins
Design Requirements
    Signals Classification
    Self -sustained
Economic Requirement
  Stayed within budget
ISO/IEC 25012 - Quality of Data
  Accuracy, Consistency, Credibility
ISO/IEC 25064 - User Needs Report
  Accommodating User’s needs by reporting necessary data that is useful
COVID-19
Precautions and Prevention
    Masks and Weekly Tests
    Transferring of equipment
    Stayed at least 6 feet apart
    Avoid crowds and poorly ventilated space

## Slide 21: Future Work
Immediate Work
Dataset Library
    Improve library by collecting new dataset in different environments
Battery
    New battery to improve system sustainability
Filter/Amplifier PCB
    Amplifier for weaker/low vibration signals
    Increase range of sensors
Data Processing
    Increase the number of features
Potential Improvements
Wireless Geophones
  Greatly improve range and flexibility of the system
Cameras
  Adding more functionality to the system such as image classification and/or facial recognition
Accoutic Sensors
  Detect and classify sound

## Slide 22: Acknowledgements
Our group would like to acknowledge the input and support of our Customer Mentor: William Shepherd and Technical Manager: Dr. Tomas Materdey
Andrew Davis for ordering parts and lab access
UMass Boston Engineering Department & Steven Institute of Technology

## Slide 23: Questions

## Slide 24: References
[1] D. H. Cross, “Terrain Considerations And DataBase Development For The Design And Testing Of Devices To Detect Intruder-Induced Ground Motion,” May-1978. [Online]. Available: https://apps.dtic.mil/sti/pdfs/ADA055602.pdf.
[2] Rubin, Marc & Camp, Tracy & van Herwijnen, Alec. (2012). Automatically Finding Avalanches in Geophone DataL A Pattern Recognition Workflow. International Snow Science Workshop (ISSW).
[3] “Signal Processing and Machine Learning Techniques for Sensor Data Analytics - Video,” Video - MATLAB. [Online]. Available: https://www.mathworks.com/videos/signal-processing-and-machine-learning-techniques-for-sensor-data-analytics-107549.html. [Accessed: 19-Apr-2021].
[4] “Designing and Implementing Real-Time Signal Processing Systems Video,” Video - MATLAB. [Online]. Available: https://www.mathworks.com/videos/designing-and-implementing-real-time-signal-processing-systems-1502972724722.html. [Accessed: 19-Apr-2021].
[5] KAFADAR, O. A geophone-based and low-cost data acquisition and analysis system designed for microtremor measurements In-text: (Kafadar, 2020) Your Bibliography: Kafadar, O., 2020. A geophone-based and low-cost data acquisition and analysis system designed for microtremor measurements. Geoscientific Instrumentation, Methods and Data Systems, 9(2), pp.365-373.
[6] N. Evans and D. Chesmore, “Automated Identification of Vehicles using Acoustic Signal Processing,” The Journal of the Acoustical Society of America, vol. 123, no. 5, pp. 3342–3342, 2008.
[7] Scikit-learn: Machine Learning in Python, Pedregosa et al., JMLR 12, pp. 2825-2830, 2011.