## Slide 1
System of Networked Sensors for Detection and
Characterization of Underground Activity Augustus Standeven, Tyler McKean, Vulindsky Fanfan, Yohannes Kidane
Department of Engineering – University of Massachusetts Boston
Commercial security systems are expensive, complex, time consuming to setup, and can be difficult to interpret.
Goal: Create a security system that is portable, cheap, easy to setup, and user-friendly with intentions that project could be scaled up for another Design team in the future.
Underground Security Detection Systems
Data Acquisition
Geophone sensors to capture ground vibrations
PCB to acquire full oscillation information
Arduino Due
Analog-to-Digital Conversion
Raspberry Pi
Data Logging, Processing, and Display Results to Display
Power Brick Battery daisy-chains power to components
The system is composed of four subsystems:
Geophone Sensors with DC Offset PCB
Passive Vibration sensors will be offset by 1.65V to capture peaks and troughs of oscillations.
Arduino Due
12-bit Resolution for A/D Conversion
Sample Rate at 500Hz
Serial communication via USB port to Raspberry Pi for data logging.
Raspberry Pi
Data logging of Serial data from Arduino.
Python scripts that Preprocess logged data and Extracts Statistical and Analytical Features that are imported into a KNN Machine Learning Model.
Displays predictions of Vibrations to GUI, which includes History tab for previously occurred events.
Power Brick Battery
Provides 12V 6000mAh/5V USB DC voltage
Networked Sensors System featuring:
Low Cost, Portable, Minimal Size system that’s simple to setup
Machine Learning model trained for 5 different vibration classes with an accuracy range of 80-90% in static setup
GUI displaying Accuracy and History of Predictions to Rpi 4” LCD screen
Power Brick Battery that can self-power system for about 10-11 hours
Project could be expanded by incorporating real-time processing, scaling up number of sensors, including filters/amplifiers to sensors, and increasing signal library to train model to classify more vibration sources
MOTIVATION
PROJECT DEFINITION
DESIGN DESCRIPTION
DESIGN VALIDATION
FINAL PRODUCT, CONCLUSIONS & FUTURE PLAN
References
4/30/21 Acknowledgements
GUI displays 89% accuracy for 1200 observations of 5 vibration classes
MATLAB Classification Learner set KNN model’s accuracy 80-85%
Python’s individual accuracy for 5 different class of vibrations
Our group would like to acknowledge the input and support of our Customer Mentor: William Shepherd and Technical Manager: Dr. Tomas Materdey
Power Brick at full charge, system was able to capture data values for about 11 hours